## Slide 1: Surveying I.
Positioning. Elevation, height, height measurements. The principle of optical levelling. The structure of the surveyors’ level.
Created by Dr. Szabolcs RÓZSA
Lecturer: Dr. Lóránt FÖLDVÁRY
September 11, 2023.

## Slide 2
Surveying vs Geodesy
Geodesy: the determination of the shape and the size of the Earth and its gravity field. To provide the fundamentals of positioning (control networks, etc.)

## Slide 3
Surveying vs Geodesy
Surveying: the determination of the location and the shape of natural or man-made objects on the ground (or above/below) (survey), and present the results numerically or graphically (mapping) and the localization of the characteristic points of planned structures on the field (stake out/set out).

## Slide 5
What can happen, when no surveyors are available on site?

## Slide 6
What can happen, when no surveyors are available on site?

## Slide 7
What will this course provide you?
You’ll start thinking as a civil engineer.
Knowledge on Land Surveying:
      You’ll be able to carry out smaller surveying works.
      You’ll be able to communicate your goals with the surveyor and you’ll understand his answers.

## Slide 8
Assessments
MT1 max. 20 points (min. 10 is required)
MT2 max. 20 points (min. 10 is required)
PT passed/failed (requirement: pass)
-------------------------------------
Sum: max. 40 points (min. requirement is 20)
Exam: max. 60 points (min. requirement is 30)
Final grade:
failed (1) 0 - 49 points
pass (2) 50 - 62 points
satisfactory (3) 63 - 75 points
good (4) 76 - 87 points
excellent (5) 88 - 100 points

## Slide 9
Textbooks, notes
1. Bannister-Raymond-Baker: Surveying
2. Draft notes of the Lectures + slides
http://edu.epito.bme.hu
3. Electronic handouts for the practicals
http://edu.epito.bme.hu
4. Last, but not least: YOUR OWN NOTES TAKEN ON THE CLASSES!

## Slide 10: Surveying I.
Positioning. Elevation, height, height measurements. The principle of optical levelling. The structure of the surveyors’ level.
Created by Dr. Szabolcs RÓZSA
Lecturer: Dr. Lóránt FÖLDVÁRY
September 11, 2023.

## Slide 11
Surveying vs Geodesy
Geodesy: the determination of the shape and the size of the Earth and its gravity field. To provide the fundamentals of positioning (control networks, etc.)
Surveying: the determination of the location and the shape of natural or man-made objects on the ground (or above/below) (survey), and present the resutls numerically or graphically (mapping) and the localization of the characteristic points of planned structures on the field (stake out/set out).

## Slide 12
Geodesy
What is the shape of the Earth?

## Slide 13
Geodesy
1735

## Slide 14
Geodesy
The gravity field

## Slide 15
Geodesy
The equipotential surfaces of the gravity field and the plumbline

## Slide 16
Geodesy
The equipotential surfaces of the gravity field and the plumbline

## Slide 17
The physical (real) shape of the Earth:
the boundary surface formed by the surface
of the continents (topography) and the sea surface.
→ geoid
The theoretical (mathematical) shape of the Earth:
the surface defined by open water bodies when only the gravity has an effect
on it (equipotential surface)
infinite number of equipotential surfaces
-> the one that coincides with the mean sea level
The shape of the Earth

## Slide 18
What is the mean sea level?
Time series of the Triest tide gauge (1875-2018)

## Slide 19
Positioning
Coordinate system:
      Fitted to the appropriate reference surface (ellipsoid, sphere, plane)

## Slide 20
Projections in Geodetic and Plane Surveying
Geodetic surveying
Plane surveying

## Slide 21
h = N + H
→ N the distance between the geoid and the ellipsoid (geoid undulation) -> determined by geodesy
→ H the height above the geoid (the mean sea level)
Determination of the height above the ellipsoid:

## Slide 22
What do we mean by height? What should the height of a point express?
In which direction does the water flow between A and B?

## Slide 23
What do we mean by height? What should the height of a point express?
Solution: water flows from A to B!
Heights should express the potential level of the point
Thus:
[m2/s2]
Height systems:
[m]

## Slide 24
The definition of the reduced level (RL)
Reduced level: the height of the point above a chosen reference mean sea level, called the Datum.

## Slide 25
Measuring height differences:
levelling:
- the infinitesimal parts of the level surface are used
(hydrostatic levelling – law of communicating vessels)
- the tangent plane of the level surface is used
(optical levelling),
- the vertical distances from the level surface or its tangent plane are measured
trigonometric heighting
- the height difference is calculated by observing a distance and an elevation angle
in a right triangle in the vertical plane
physical heighting
- Physical quantities are measured, which are related to elevations (e.g. barometric
heighting)

## Slide 26
P
Q
lP
lQ
DP
DRLPQ
(lP)
DQ
(lQ)
topography
Level surface of P
dP
dQ
Level surface of Q
Level surface of instrument
The principle of optical levelling
Line-of-sight (height of collimation)

## Slide 27
→
P
Q
lP
lQ
DP
DRLPQ
(lP)
DQ
(lQ)
topography
Level surface of P
dP
dQ
Level surface of Q
Level surface of instrument
The principle of optical levelling
Line-of-sight (height of collimation)
-

## Slide 28
The structure of the tilting (dumpy) level
tribrach
Alidade / upper part

## Slide 29
The principle of astronomical telescopes

## Slide 30
The structure of surveyors’ telescope
Surveyors’ telescope with external focusing

## Slide 31
The structure of surveyors’ telescope
Surveyors’ telescope with internal focusing

## Slide 32
The parallax
The phenomena of parallax
Note that in case of parallax, the reading changes depending on the position of the observer.

## Slide 33
The measurement of height differences using surveyors’ level

## Slide 34
The levelling staff
Staff reading: 1664
stadia lines
Horizontal crosshair

## Slide 35
Measuring instrument-staff distance with the stadia lines
Reading on the upper
stadia line: 1743
Reading on the lower
stadia line: 1586
stadia lines

## Slide 36
Measuring instrument-staff distance with the stadia lines
Levelling staff
d
c
z
1743
1586
Reading on the upper
stadia line: 1743
Reading on the lower
stadia line: 1586

## Slide 37
Levelling staff
d
c
z
1743
1586
Reading on the upper
stadia line: 1743
Reading on the lower
stadia line: 1586
Measuring instrument-staff distance with the stadia lines

## Slide 38: Thank You for your Attention!