## Slide 1: Surveying I.
The structure of the tilting and the automatic level. Electronic levels. Adjustment of the surveyors’ level. Systematic error sources of levelling. Line levelling and Detail point levelling. The Rise&Fall and the Height-of-Collimation methods.
September 25, 2023
Created by Dr. Szabolcs RÓZSA
Lecturer: Dr. Lóránt FÖLDVÁRY

## Slide 2
The structure of the tilting level

## Slide 3
Levelling the instruments
bubble tube
bull’s eye bubble

## Slide 4
bull’s eye bubble or round/circular bubble
Levelling the Instruments
Sensitivness of bubble tube:
bubble tube

## Slide 5
Structure of the tilting level

## Slide 6
Structure of the tilting level

## Slide 7
Structure of the tilting level
Prism
The levelling bubble is tilted
The levelling bubble is horizontal
Levelling bubble
Levelling the instrument – the prismatic reader
Levelling bubble

## Slide 8
The Adjustment of the tilting level

## Slide 9
1. The round bubble must be adjusted to the standing axis
The adjustment of the tilting level
The normal point: its tangent is perpendicular to the standing axis.

## Slide 10
1. The round bubble must be adjusted to the standing axis
The Adjustment of the tilting level
→
and
- Position of the bubble
- Position of the bubble
The normal point: its tangent is perpendicular to the standing axis.

## Slide 11
1. The round bubble must be adjusted to the standing axis
After levelling the instrument with the levelling bubble (on the top of the telescope) in two perpendicular direction, the round bubble can be adjusted.
The adjustment of the tilting level
The normal point: its tangent is perpendicular to the standing axis.

## Slide 12
2. The horizontal crosshair (chh) must be perpendicular to the standing axis (v)
3. The levelling bubble (llb) must be adjusted to the line-of-sight (J): the collimation error must be checked (two-peg test)
The Adjustment of the tilting level

## Slide 13
The two-peg test (part 1)
The Adjustment of the tilting level

## Slide 14
The two-peg test (part 2)
Adjustment:
The Adjustment of the tilting level

## Slide 15
Automatic Level

## Slide 16
Automatic level
Central ray
control

## Slide 17
1. The round bubble must be adjusted to the standing axis
The adjustment of automatic levels
2. The horizontal crosshair must be perpendiculat to the standing axis
Using a bubble tube placed temporarily on the instrument
3. Collimation error
The collimation error is caused by the faulty operation of the compensator. It is proportional to the tilting angle of the standing axis. This error occurs, when the standing axis is not vertical. It can be tested by creating various tilted standing axis and measuring the height difference between points.

## Slide 18
Mitigating the effect of Systematic Error
  Eliminate the cause (e.g. adjustment of the instrument). Drawback: have to mitigate the total effect.
  Applying observation procedure that eliminates the effect of the systematic error.
  The quantification of the error and the correction of the raw observations. Used in automatic instruments, when the built-in computer can do the calculations automatically.

## Slide 19
The systematic error sources of levelling
Which error accumulates when the observed rise/fall values are added up?
2. How could the individual systematic error sources be mitigated most effectively?
3. What kind of rules and procedures must be followed to minimize the effects of systematic error in the results?

## Slide 20
The systematic error sources of levelling
The effect of curvature is caused by the curvature of the level surface. It affects the observed elevation difference when the instrument is not set up equidistantly from the staves. When the station is equidistant from the staves, the error will not accumulate.
The collimation error can be caused by
  Misalignment of the levelling bubble; is eliminated by observing equidistant staves;
  Inaccurately levelled levelling bubble: the effect does not accumulate
  One-sided heat: can accumulate (sun shines from the same side of the levelling line) -> the instrument should be protected by a surveying umbrella
Instrument

## Slide 21
The systematic error sources of levelling
3. The collimation error of automatic levels: this error can accumulate in longer levelling lines. The instrument must be levelled perfectly or the observations should be done twice (BFFB) with relevelling the instrument between the BF and FB readings.
Instrument

## Slide 22
4. The offset of the trunnion axis: accumulates in the height differences. The error is caused by a tilted standing axis. By turning the level toward the BS and the FS staves, the level of the line-of-sight changes. A vertical standing axis (accurately levelled instrument) minimize this effect.
The systematic error sources of levelling
Instrument

## Slide 23
5. The index error of the staff means that the index (0 graduation) does not coincide with the bottom of the staff. The error is eliminated using a single staff, or having an even number of stations in case two staves are used.
The systematic error sources of levelling
d
Staff 1
Staff 2
Staff 1
DRL12 = [(lBS1)+d1]-[(lFS2)+d2)]=lBS-lFS+d1-d2
DRL23 = [(lBS2)+d2]-[(lFS3)+d1)]=lBS-lFS+d2-d1
Staff

## Slide 24
The graduation error of the staff can accumulate in case of large height differences. It can not be eliminated by observation procedures. The graduation must be standardized using an etalon length.
The systematic error sources of levelling
Staff

## Slide 25
7. The tilting of the staff can accumulate as well in case of large height differences when the round bubble of the staff is unadjusted. The round bubble of the staff must be adjusted.
The systematic error sources of levelling
di
a
Staff

## Slide 26
8. The subsidence of the instrument is caused by external effects. It accumulates in the observed elevation difference. The effect can be minimized by symmetric observation technique (B-F-F-B) or double-run line levelling.
9. The subsidence of the staff accumulates in the observed DRL, too. The effect can be minimized by applying fixed change points (change plates, pegs, HILTI nails) or doing double-run line levelling.
The systematic error sources of levelling
A
B
dh
lbs A
lfs B
A
B
dh
lbs A
lfs B
DRLAB=lBS A-lFS B-dh
DRLAB=lBS A-lFS B+dh
BS-FS
FS-BS
External

## Slide 27
10. The refraction has a random part, when the the mirage effect causes uncertain staff reading. The near-ground refraction can cause a systematic error affecting the observed height difference in case of large elevation differences. By following appropriate procedures, both effect can be minimized.
During levelling one must avoid the mirage effect of the atmospheric layers. Levellings are usually done in the 2-hour-period of either starting half an hour after sunrise or ending half an hour before sunset.
Near-ground refraction is minimized by limiting the lowest staff reading (min. 30-50cm) and the maximum instrument-staff distance (35-20 m) depending on the order of the levelling.
The systematic error sources of Levelling

## Slide 28
The level must be set up equidistantly between the two staves.
The instrument must be protected from direct sunlight.
In case of a tilting level: the levelling bubble must be set before each staff reading, and checked after the reading is taken!
Keep the staff firmly in a vertical position (use a round bubble)!
5. The graduation of the levelling staff must be standardized regularly!
6. Always do a double-run levelling using an even number of stations!
7. Do the levelling when the atmosphere is stable!
Procedure of Levelling

## Slide 29
Measuring the level difference between two points

## Slide 30
In case of larger distances: Line Levelling
change plates
The direction of levelling
DH
Dh1
Dh2
Dh3
Dh4

## Slide 31
.
Line Levelling
DH=Dh1+Dh2+Dh3+Dh4
The direction of levelling
DH
Dh1
Dh2
Dh3
Dh4
DH=SlBS-SlFS

## Slide 32
A
B
HA
HB=?
PID | d | BS |  | FS |  | Rise | Fall | H
A
1
1
d=20m
20
12
14
14
58
0.244
103.455
2
2
19
08
33
13
99
0.566
d=15
3
3
15
14
74
09
13
0.561
d=13
B
13
08
69
11
25
0.256
0.561
1.066
DHAB=SRise-SFall=-0.505 m
102.950
Line Levelling:
the Rise&Fall Method

## Slide 33
PID | d | BS |  | FS |  | Rise | Fall | H
A |  | 12 | 14 |  |  |  |  | 103.455
1 | 20 | 08 | 33 | 14 | 58 |  | 0.244 | 
2 | 19 | 14 | 74 | 13 | 99 |  | 0.566 | 
3 | 15 | 08 | 69 | 09 | 13 | 0.561 |  | 
B | 13 |  |  | 11 | 25 |  | 0.256 | 
B |  | 12 | 03 |  |  |  |  | 
1 | 11 | 10 | 01 | 09 | 11 | 0.292 |  | 
2 | 13 | 13 | 53 | 15 | 19 |  | -0.518 | 
3 | 18 | 15 | 22 | 09 | 41 | 0.412 |  | 
A | 22 |  |  | 11 | 97 | 0.325 |  | 
DHAB=SRise-SFall=-0.505 m
DHBA=SRise-SFall=+0.511m
Let’s compute the mean height difference:
HB=103.455-0.508=102.947m
Line Levelling:
Double-Run

## Slide 34
Detail point levelling
The determination of the reduced level of characteristic points used for other engineering tasks.
The levelling is done between two benchmarks.
Detail point levelling

## Slide 35: Detail Point Levelling
A
B
Ordnance Datum
RLA
RLB
The elevation of the characteristic points of the ditch should be determined!

## Slide 36: The Height-of-Collimation method
Height of collimation: The elevation of the horizontal line of sight. It can be computed by adding the elevation of the backsight point and the backsight reading.
A
Ordnance Datum
RLA
HoC=RLA+AlBS
AlBS
Steps of Computation:
Compute the corrected elevation of the change points!
Compute the Height of Collimation at each station!
Compute the elevation of the detail points (HoC-lIS)!

## Slide 37
A
B
Ordnance Datum
HA
HB
I1
I2
I3
101
102
103
104
PID | d | Backsight (BS) | Intersight (IS) | Foresight (FS) | Rise/Fall | Height of Collimation | Elevation
A |  | 1214 |  |  |  |  | 103.455
I1 |  | 0833 |  | 1458 |  |  | 
101 |  |  | 1104 |  |  |  | 
102 |  |  | 1421 |  |  |  | 
103 |  |  | 1428 |  |  |  | 
104 |  |  | 1067 |  |  |  | 
I2 |  | 1474 |  | 1399 |  |  | 
I3 |  | 0869 |  | 0913 |  |  | 
B |  |  |  | 1124 |  |  | 102.947
-0.244
-0.566
+0.561
-0.255
S= -0.504
S= -0.508
D=-4mm
True - Observed
(-1)
(-1)
(-1)
(-1)
103.210
102.643
103.203
104.043
102.939
102.622
102.615
102.976

## Slide 38
  Surveying I. (BSc)
  End of Lecture
  Budapesti University of Technology and Economics
Department of Geodesy and Surveying