## Slide 1: Surveying II
Point cloud survey
Photogrammetry, UAV, laser scanning
23 May, 2024

## Slide 2: Instruments of point cloud surveying
Terrestrial Laser Scanner (TLS)
Mobile Mapping System (MMS)
Airborne Laser Scanner (ALS)
Photogrammetry, UAV
LiDAR
}
Difficulties: rain, snow, dust, fog, strong sun, water puddles, window glass,
moving people, vehicles, uneven point density
homogeneous areas (e.g. water), moving leaves (wind)
Usually LiDAR measurements are supported by simultaneously
shooted photography for colouring the point cloud. Recently more and more UAVs are equipped with LiDAR.
Notes: 2
2

## Slide 3: Terrestrial Laser Scanners
Notes: 3

## Slide 4: Terrestrial Laser Scanners
Specifications
Laser beam divergence (point size e.g. 10 mm @ 100 m)
Angular resolution (point density e.g. 5 mm @ 50 m, ~20”)
Range (depends on the reflecting surface)
Speed (e.g. 100 000 pts/s)
Field of view (e.g. Hz: 360°, V: 270°)
Range accuracy (e.g. ±2-10 mm)
Built-in or external camera
video
Notes: 4

## Slide 5: „Noise” in the point cloud
Moving people
Facing the Sun
Notes: 5

## Slide 6: Airborne Laser Scanners
Specifications
Altitude (even 5000 m)
Field of view (60-75°)
Divergence (~0.2 mrad)
Range accuracy
(3 cm-30 cm depending on the altitude)
GNSS, IMU and camera as accessories
1-10 pts/m2
Notes: 6
Számoljuk ki az 1 cm átmérőjű lézersugár méretét 1000 m repülési magasság esetén:
Tan(0.0002rad) * 1000000 mm =190 mm
1 cm + 2 * 19 cm ~ 40 cm

## Slide 7: Airborne Laser Scanners
Kép: https://gis.stackexchange.com/questions/142443/what-are-lidar-returns
Specifications
Altitude (even 5000 m)
Field of view (60-75°)
Divergence (~0.2 mrad)
Range accuracy (3 cm-30 cm depending on the altitude)
GNSS, IMU and camera as accessories
1-10 pts/m2
Multiple echos
video
Notes: 7
Számoljuk ki az 1 cm átmérőjű lézersugár méretét 1000 m repülési magasság esetén:
Tan(0.0002rad) * 1000000 mm =190 mm
1 cm + 2 * 19 cm ~ 40 cm

## Slide 8: Mobile Mapping Systems
SLAM (Simultaneous Localization And Mapping)
Sensor fusion (GNSS, IMU, 2D-scanner, odometer, camera,
Ladybug camera, …)
In a vehicle, in a backpack, in hand (handheld, mobile phone)
Properties of 2D-scanners
video
Notes: 8

## Slide 9: Unmanned aerial vehicle (UAV)
Specifications
Fixed-wing and copters (4-6-8 rotor)
Flight time with one accumulator (copter) ~30 min.
Resolution (Ground Sampling Distance; GSD) depends on
the altitude and the camera
Altitude 20-100 m (administrative control)
80% frontal and side overlap
Nadir and oblique images
Structure from Motion (SfM) technique
Image Acquisition Plan
video
Notes: 9

## Slide 10: Image Acquisition Plan
MB ≤ 0.3-0.5 GSD
  motion blur (MB)
  ground sample distance (GSD)
overlap (~80%)
nadir or oblique imagery
sensor width (sw)
focus (f)
altitude (h)
footprint width (dw)
velocity (v)
overlap (o)
iw – image width [pixel]
ss – shutter speed [sec]
Notes: 10

## Slide 11: Comparison of Technologies
Price: UAV (600-30.000 EUR) – TLS (30.000-120.000 EUR) – MMS (300.000 EUR) – ALS
LiDAR provides points on homogeneous surfaces as well, photogrammetry cannot.
LiDAR provides point cloud directly, UAV photos are processed for a point cloud
UAV, ALS less sensitive for masking
Survey of linear facilities: MMS
Survey of building interiors: TLS
Topography survey of large area: ALS
Survey of small area (1-20 ha): UAV
Photogrammetry
LiDAR
Notes: 11

## Slide 12: Data stored in point clouds
Position x, y, z
RGB colour or grayscale
Intensity
Scanning angle
Normal (Nx, Ny, Nz)
Scalar (e.g. classification)
More positions due to multiple echo
...
Notes: 12

## Slide 13: Pre-processing of point clouds
Registration, georeference
Transformation into the geodetic system, registration of point
clouds from multiple TLS stations, 3D transformation;
at least 3 control points required
ICP algorithm - Iterative Closest Point; register a point cloud
to a registered one
Notes: 13

## Slide 14: Pre-processing of point clouds
Noise reduction (averaging, surface matching, statistical method)
An example for a statistical method:
For each points, calculating the mean distance of the nearest 10 neighbours, dave, then determining the average, a, and the standard deviation, σ.
Notes: 14

## Slide 15
noisy
point
cloud
Notes: 15

## Slide 16
after
statistical
filtering
Notes: 16
A statisztikai alapú szűrő minden pontra meghatározza K legközelebbi szomszéd távolságát, ha az átlagos távolság a szórás valahányszorosával növelve nagyobb mint egy korlát, akkor kihagyja a pontot.
K és a szórás szorzója input adat.

## Slide 17
after
surface
based
filtering
Notes: 17
A felület alapú szűrés a pont környezetébe eső pontokra (adott sugár vagy K legközelebbi) egy legjobban illeszkedő síkot számít és a vizsgált pont távolságát hasonlítja egy adott limithez.

## Slide 18: Pre-processing of point clouds
Classification: ground, vegetation, building, water, etc.
Segmentation:
  edge-based (edge detection, area bounded by edges)
  region-based (starting from a point, and observing neighbours with similar properties)
  model fitting
  machine learning
Notes: 18
A szegmentálási módszerek azonos tulajdonságú csoportok összefüggő pontcsoportok kialakítására törekednek. Például a területnövelő módszerek esetén normális/gradiens alapján, ameddig a változás
A szegmenseket osztályokba sorolják a tulajdonságuk alapján

## Slide 19
Classified point cloud (ALS)
Notes: 19

## Slide 20
and the reality ...
Notes: 20

## Slide 21
and the reality ...
Notes: 21

## Slide 22: Derived products
DSM – Digital Surface Model (based on the first echo)
DTM – Digital Terrain Model (based on the last echo)
nDSM – normalized Digital Surface Model (DSM - DTM)
reality
Notes: 22

## Slide 23: Derived products
Ortophoto
True ortophoto
Point cloud views
top view and profile
Mesh model
Notes: 23

## Slide 24: Derived products
Ortophoto
True ortophoto
Point cloud views
top view and profile
Mesh model
Notes: 24

## Slide 25: Derived products
Ortophoto
True ortophoto
Point cloud views
top view and profile
Mesh model
Notes: 25

## Slide 26: Derived products
Ortophoto
True ortophoto
Point cloud views
top view and profile
Mesh model
Notes: 26

## Slide 27: Applications
Design map, point cloud / ortophoto evaluation e.g. AutoCAD MAP/Civil software ortophoto and evaluated map: http://www.agt.bme.hu/maps/gmap.php?config=barnag
Notes: 27

## Slide 28: Applications
Evaluation in AutoCAD Civil 3D (Recap)
Notes: 28

## Slide 29: Applications
Measurement in the point cloud (CloudCompare)
Notes: 29

## Slide 30: Applications
Volume calculation
Notes: 30

## Slide 31: Applications
Building/object modelling (triangular mesh)
Notes: 31

## Slide 32: Applications
Quality control
Notes: 32

## Slide 33: Thank you for the attention!