## Slide 1
Lecture 10.
GNSS error sources. Application of GNSS in Surveying. GNSS infrastructure. Transformation into national reference system.
Sz. Rózsa, L. Földváry, Sh. Manguri

## Slide 2
Accuracies / Error sources
Differential GPS (DGPS)
Applications in Surveying
GNSS infrastructure
Transformation into national reference system
Contents

## Slide 3
Error sources – signal propagation
  The atmosphere has an impact on the signal propagation path.
  Troposphere and Ionosphere
Ionosphere
  The Ionosphere (70-1000 km elevation) contain electrons and ions, which have an effect on the propagation of electromagnetic signals.
  the delays depend on the frequency;
Accuracy and error sources

## Slide 4
Troposphere
  Up to 40-70 km (tropospheric refraction)
  Meteorological factors (weather, air pressure, temperature, etc.)
  Empirical models
Multipath
  GPS signals are reflected, and direct and indirect signals are also received.
Direct
Indirect
Accuracy and error sources

## Slide 5
Error sources – receiver error
  thermal noise
  receiver clock corrections
  antenna phase center offsets and variations
Accuracy and error sources

## Slide 6
Error sources – satellite geometry
  Not all of the satellite constellation enables the optimal positioning.
  DOP – „Dilution of Precision“
dr accuracy of the pseudorange observation
dPOS accuracy of the positioning
PDOP: Position (3D) Dilution of Precision is the reciprocal value of the volume of a tetraeder defined by 4 satellites + the receiver.
Accuracy and error sources

## Slide 7
Bad
Good
Accuracy and error sources
PDOP high
PDOP low

## Slide 8
Accuracies / Error sources
Differential GPS (DGPS)
Applications in Surveying
GNSS infrastructure
Transformation into national reference system
Contents

## Slide 9
To enhance the accuracy of positioning, the DGPS method could be used.
Reference station with accurate coordinates
The receiver computes its own position
Reference computes the corrections
Reference broadcasts the corrections
Differential GPS

## Slide 10
Reference station with accurate coordinates
the receiver computes its own position
the reference computes the corrections
the reference broadcasts the corrections
the rover determines corrected position
Differential GPS

## Slide 11
Accuracies / Error sources
Differential GPS (DGPS)
Applications in Surveying
GNSS infrastructure
Transformation into national reference system
Contents

## Slide 12
The relation between phase, range and wavelength:
The phase repeats itself after
the phase angle of 2p.
It can be written as:
where N = 0,1,2,3,… (integer numbers)
Phase observations

## Slide 13
Therefore to compute the range from the phase observations, we can use the following formula:
where N is the phase ambiguity.
Phase observations

## Slide 14
Only the phase angles can be measured, the ambiguity is not known.
Ambiguity = The number of full waves between the satellite and the receiver.
Another reference station is needed to compute the ambiguity parameters.
In surveying relative positioning is used (instead of absolute positioning): Base station + Rover station
Phase observations

## Slide 15
Static GPS Observations
  At least two receivers
  The base station is set up on a control point (known coordinates)
  The rover station is set up on an unknown point.
  same receiver configuration of base and rover
  Time span:
        1 freq.: 30 min+ 5 min/km (up to 10 km)
        2 freq: 20 min + 5 min/km
  Accuracy: 1 cm or better (for longer observations even 1-2 mm in a distance of 15 km)
Static GPS observations

## Slide 16
Kinematic observations
  At least two receivers
  Base receiver on a control point
  Rover station must be initialized (at least 20 min on the same point)
  Afterwards the rover can survey the points.
  time span: 5-10 secs per point
  At the end of the survey (and after signal outage), the initialization should be repeated.
Kinematic observations

## Slide 17
Real-Time Kinematic Observations
  At least two receivers (preferably 2 freq.)
  Base on a control point.
  Real time data broadcasting (phase observations and base coordinates) between base and rover (radio, GSM, internet)
  Cca. 1-5 min to determine the ambiguity parameters
  after the solution of the ambiguity parameters, the unknown points can be measured.
  time span: 2-3 sec per point
Real-time kinematic observations

## Slide 18
Post-processing vs real-time
Post processing:
static observations
kinematic observations
Real-time:
real time kinematic

## Slide 19
Network Observations
Radial configuration
Network configuration

## Slide 20
Point reconnaissance
How should the place of the points be selected?
a clear view to the sky;
free of electromagnetic interference (no high voltage wires in the vicinity);
the point should be in public area, close to roads;
the stability of the points should be ensured.
The selected stations should be marked, the position of the obstructing objects should be noted

## Slide 21
Planning the observations
in case of obstructing objects, or high accuracy requirements, the observations can be planned;
planning software predicts the number of visible satellites, the PDOP values by knowing the approximate positions of the satellites and the approximate station coordinate. Trimble GNSS Planning Tool (Online)
The position of obstructed objects can be added to the planner software, thus the effect of the obstructed sky can be estimated.
Using the PDOP values, the suitable time window can be selected for the observations.

## Slide 22
Accuracies / Error sources
Differential GPS (DGPS)
Applications in Surveying
GNSS infrastructure
Transformation into national reference system
Contents

## Slide 23
GNSS Infrastructure
Positioning in Surveying:
relative positioning can provide the sufficient accuracy;
base stations are required;
using a base-rover pair for positioning is not effective;
Solution:
continuously operating reference stations (CORS);
act as a base station, but broadcasts corrections to many rovers at the same time;

## Slide 24
Real-Time Kinematic Observations
  One-base RTK autonomous: traditional RTK
GNSS Infrastructure
  One-base RTK autonomous: service-based RTK
  Network RTK

## Slide 25
Generations of GNSS Infrastructure
1st Generation:
Permanent stations, which log the received data for post processing only. Data can be downloaded from the internet, and rover observations can be processed with these downloaded data.
2nd Generation:
Permanent stations, which log the received data, but broadcast it in real-time, too. Data can be used for post-processing and real-time application as well. Real-time kinematic positioning is achieved by a single base station.
RTK (3 cm) up to 35 km from the reference stations (in case of 2 frequencies)

## Slide 26
3rd Generation:
A network of permanent stations, which broadcasts the data to a processing facility. This facility monitors and models the systematic error of positioning (ionosphere, troposphere, orbit and clock error, etc.).
These models are used for the positioning as well.
Two concepts:
Area Correction Parameters (ACP): The effect of the error sources are interpolated on a surface. The parameters of the surface is broadcasted to the rover receiver, thus it can apply the correction by knowing its own position
Virtual Reference Station (VRS): The observations of a virtual reference station in the vicinity of the rover are estimated, and broadcasted to the user.
Generations of GNSS Infrastructure

## Slide 27
Active GNSS networks:
National examples:
SAPOS, Germany
SWEPOS, Sweden
gnssnet.hu, Hungary
… etc.
Active GNSS networks
Notes: https://www.sapos.de/

## Slide 28
The Hungarian Active GNSS Network
PENC

## Slide 29
Augmentation Systems
Ground based (GBAS):
The GNSS Infrastructure, the network of continuously operating reference stations and the processing facility.
The corrections are broadcasted through radiolink or the internet.
Satellite based (SBAS):
A network of ground based stations to monitor the systematic error sources, effects are modelled, and corrections are broadcasted to geostationary satellites, which transmit a GPS like signal to the GNSS receivers (EGNOS, WAAS, etc.)

## Slide 30
Augmentation Systems
Ground based (GBAS):
Regional contribution: EUPOS
Notes: https://www.sapos.de/

## Slide 31
Augmentation Systems
Notes: The information provided by all these regional SBAS systems, improves the accuracy and reliability of GNSS positioning while also providing a crucial integrity message.

## Slide 32
 | WAAS | EGNOS | MSAS | GAGAN
Number of geostacionary satellites | 4 | 3 | 2 | 3
Longitude | W53, W98, W120, W178 | W15, E64, E21 | E140, E145 | E34, E83, E132
Semiaxis of orbital plane [km] | 42 164 | 42 164 | 42 164 | 42 164
WAAS (Wide Area Augmentation System) – USA
EGNOS (European Geostationary Navigation Overlay Service) – Europe
MSAS (Multifunctional Satellite-Based Augmentation System) – Japan
GAGAN (GPS and Geo Augmented Navigation System) – India
Augmentation Systems
Notes: There are four official free of charge SBAS systems: EGNOS in Europe, WAAS in the USA, MSAS in Japan and GAGAN in India.
These all are civil-controlled regional systems and there is a form of coordination to ensure that they are interoperable to provide a seamless worldwide navigation system.
SBAS GEO satellites provides GPS look-alike signals and GPS corrections to improve positioning accuracy to around 1 metre horizontally and 3 metres vertically (or better).
Timing accuracy is enhanced to better than 10 nanoseconds.

## Slide 33
Regional systems
Global systems
Augmentation systems
Basic and Augmentation Systems

## Slide 34
Accuracies / Error sources
Differential GPS (DGPS)
Applications in Surveying
GNSS infrastructure
Transformation into national reference system
Contents

## Slide 35
Transforming the GPS coordinates
GPS observations refer to the WGS-84 coordinate system.
Local coordinate grids are linked with a local ellipsoid, which
    usually not geocentric;
    has different size than the WGS-84 ellipsoid.
a link should be established between the two systems to be able to compute the grid coordinates from the WGS-84 ones
Coordinate Transformation

## Slide 36
Transforming the GPS coordinates
Common points in both coordinate systems (local and WGS-84) are needed.
In rectangular coordinate systems the 3D Helmert-transformation can be used to compute the coordinates in the local system:
Where:
x,y,z are the local cartesian coordinates;
DX, DY, DZ are the elements of the translation vector;
X,Y,Z are the WGS-84 cartesian coordinates;
R is the rotation matrix;
m is the scale factor.

## Slide 37
Transforming the GPS coordinates

## Slide 38
Thank You for Your attention!