## Slide 1
Dr. László Koncsos
Modeling of environmental systems

## Slide 2
General information I.
Lecturer: Dr. Laszlo Koncsos
Dept. of Sanitary and environmental engineering
Building K gf. 45

## Slide 3
Subject requirements
    2 lecture – basics in mathematical modelling, transport models
    1 lecture – air pollution
    2 lecture – integrated modelling, unsaturated soil zone
    1 lecture – statistical modelling
    2 lecture – Models of wastewater treatment, artificial intelligence
    Mid year test (9. week)
    4 exercise (11-14)
    The semester is successful if the audit test is successful and the homework has been submitted by the student on time
General information II.

## Slide 4
Environmental modeling overview
  clarifying basic concepts
  modeling process overview
    In general
    Through examples
    introducing problem sources
Goals

## Slide 5
Human activity
Air
Water
Soil
Wildlife
Artificial env.
Human
Ecosystem
Urban environment
Landscape
Why you need to model?

## Slide 6
General transport equation and its applications

## Slide 7
Transport equations:
Mathematical description of the law of material balance in liquids
A mass balance, also called a material balance, is an application of conservation of mass to the analysis of physical systems. By accounting for material entering and leaving a system, mass flows can be identified which might have been unknown, or difficult to measure without this technique.

## Slide 8
Transport equation
Need of application
The load of pollutants to the various ecosystem components (i.e. the soil, surface water and air) and the movement of pollutants from the point of emission to other components of the ecosystem, either by convection or diffusion, leads to the dispersion of these pollutants in various environmental components. Depending on the strength of the transport mechanisms, concentration gradients of these pollutants will build up in the different environmental compartments. If the pollutant concentration in certain regions of the ecosystem exceeds certain limits, an adverse effect on the flora and fauna of the ecosystem can be assumed; over the long-term this can threaten the sustainability of the ecosystem.
There is a need emerged to predict the pollutant concentration fields which result from different pollution sources in the ecosystem.
This requires the solution of the convection dispersion equation for the whole domain containing the sources and the receptors.
In next steps a derivation of this generaly used equation will be presented.

## Slide 9
Where
Flow velocity (vector):
Derivation of transport eq.
1.Explanation of markings:
…symbolic vector
Flow velocitiy is assumed to be changing in space and time
…Flux of mass
(Definition of fluxes : transported mass/unit surface/unit time [kg/m2/s])
C…mass concentration [g/m3]
vector operations
div -> divergence: is a vector operator that operates on a vector field, producing a scalar field
grad -> is a vector operator that operates on a scalar field, producing a vector field

## Slide 10
Derivation of transport eq.
2.Two components are concerned:
Advection: transport by fluid movement,
Diffusion: transport by molecular diffusion
Molecular diffusion often simply called diffusion, is the thermal motion of all (liquid or gas) particles at temperatures above absolute zero. The rate of this movement is a function of temperature, viscosity of the fluid and the size (mass) of the particles.

## Slide 11
Derivation of transport eq. 3.DIFFUSION: FICK’S LAW
c1
c2

x


- c1  c2
- valve opened
- Concentration equalization (Brownian motion)
FLUX of diffusion:
D – molecular diff.coef. [m2/s]
~
Fick's experiments dealt with measuring the concentrations and fluxes of conservative substance , diffusing between two reservoirs through tubes of water. It is notable that Fick's work primarily concerned diffusion in fluids, because at the time, diffusion in solids was not considered generally possible.

## Slide 12
5. Understanding transport eq.: Gauss theoreme
In vector calculus, the divergence theorem, also known as Gauss's theorem or Ostrogradsky's theorem, is a theorem which relates the flux of a vector field through a closed surface to the divergence of the field in the volume enclosed. More precisely, the divergence theorem states that the surface integral of a vector field over a closed surface, which is called the flux through the surface, is equal to the volume integral of the divergence over the region inside the surface. In the engineering fields, it is usually applied in three dimensions. However, it generalizes to any number of dimensions.
material entering and leaving a system
Definition of fluxes :
transported mass/unit surface/unit time [kg/m2/s]
Two components are concerned:
Advection: transport by fluid movement,
Diffusion: transport by molecular diffusion

## Slide 13
Definition of fluxes:
transported mass/unit surface/unit time [kg/m2/s]
Advection: transport by fluid movement,
Diffusion: transport by molecular diffusion
(C…concentration,
U…flow velocity,
D…diffusion coefficient)
6.Derivation of transport eq.
material entering and leaving a system
Changes of mass in time
within the closed surface

## Slide 14
fluxes
Basic eq.
Flux of advection
Flux of diffusion
7. Non conservative substances
For conservative substances: The mass of the system must remain constant over time, as the system's mass cannot change, so quantity can neither be added nor be removed. Therefore, the quantity of mass is conserved over time.
For non conservative substances biochemical reactions influence the concentration
Term of reactions

## Slide 15
Brownian motion
x
(1827)
Brownian motion is the random motion of particles suspended in a medium (a liquid or a gas). This pattern of motion typically consists of random fluctuations in a particle's position inside a fluid sub-domain, followed by a relocation to another sub-domain. Each relocation is followed by more fluctuations within the new closed volume.
Understanding diffusion
x…particle position (coordinate), m…mass of particle
m

## Slide 16
// *x
1.Newton equation for individual particle
random force (due to thermal molecular motions)
friction force (Stokes law)

## Slide 17
//The eq. was averaged for all particles, and
Equipartition theorem was used:
no correlation assumed between coordinates and random forces
In classical statistical mechanics, the equipartition theorem relates the temperature (T) of a system to its average energies. (k…Boltzmann contant)

## Slide 18
//with using new variable the following eq.
can be rewriten
Math. solution (analitical):

## Slide 19
M()...Averaging of a random variable
What is the variance?
Variance of a random variable:
if
then
(Einstein(1905))
The variance of spatial coordinates is a function of temperature (T) and time (t)
Standard deviation of spatial coordinates in time

## Slide 20
Derivation of spatial density function of particles:
(Einstein (1905))
This solution of the above partial diff. Eq.
is the Normal distribution
It plays a central rolle in the diffusion theory

## Slide 21
Scalar form of 3D advection diffusion eq.
vectorial form of transport eq. (see above)
Scalar form of transport equation
vectorial form of equations can be describe in scalar one

## Slide 22
x, y, z directions (3D):
D – Molecular diffusion coefficient
in water: about 10-4 m2/s
Advection: depending on the flow rate, particles with different concentration values move to varying degrees relative to each other.
Diffusion: mixing of adjacent water particles with each other, concentration leads to equalization

## Slide 23
All fluid flow is classified into one of two broad categories or regimes. These two flow regimes are laminar flow and turbulent flow. The flow regime, whether laminar or turbulent, is important in the design and operation of any fluid system. The amount of fluid friction, which determines the amount of eenergy required to maintain the desired flow, depends upon the mode of flow. This is also an important consideration in certain applications that involve pollutant transport to the fluid
Laminar and Turbulent Flow

## Slide 24
The Reynolds number is the ratio of inertial forces to viscous forces within a fluid
Turbulent or laminar flow?
The Reynolds number (Re) helps predict flow patterns in different fluid flow situations. At low Reynolds numbers, flows tend to be dominated by laminar (sheet-like) flow, while at high Reynolds numbers flows tend to be turbulent. The turbulence results from differences in the fluid's speed and direction, which may sometimes intersect or even move counter to the overall direction of the flow
v…velocity
d…turbulenth length
…kinematic viscosity

## Slide 25
Flows
Lamiar flow: smooth and orderly
Turbulent: random, slumping, disordered
t
v
v average
v’ deviation, pulsation
T
time scale of turbulence
v
O

## Slide 26
TRANSPORT
Advection flux : vc [ kg/m2s ] (v…velocity, c…concentration)
HOW DOES THE ADVECTION FLUX
DEVELOP IN TURBULENT FLOW?
0
0
?

## Slide 27
TURBULENT DIFFUSION
v
turbulent diffusion
molecular diffusion
Dtx, Dty, Dtz >> D
turbulent diffusion coefficients
in x,y,z directions

## Slide 28
3D transport equation in turbulent flow:
Dx = D + Dtx, Dy = D + Dty, Dz = D + Dtz
Advection
Diffusion
Turbulent diffusion
Random fluctuations in speed (pulsations)
To be treated as a mathematical diffusion process
Advective transport!
Time averaging(T)

## Slide 29
Simplifications
of transport equation

## Slide 30
Shallow lakes (application of 2D eq.)

## Slide 31
Depth integrated 2D convection diffusion equation
Lakes, bays
x
y
h...depth

## Slide 32
DISPERSION (explanation of the concept)
Average depth speed
v
O
v
H
After the mathematical expression of the convective term (vC):
We integrate along depth: (3D2D):
dispersion
z
x
Vertical velocity profile

## Slide 33
2D transport equation in turbulent flow :
Dx*, Dy* 2D turbulent dispersion factors of equation(Taylor)
Average taken along depth(H)
1D transport equation in turbulent flow :
Dx** 1D turbulent dispersion factor of equation
Average for cross-section area(A)

## Slide 34
DISPERSION
Convective transport due to spatial velocity differences (faster or slower than average residual particles)
v
Only in 2D or 1D equations!
  Dispersion factor: Function of the velocity distribution (hydraulic characteristics, geometry, etc.) In a more irregular watercourse, it is larger,
  Dx* = Ddx + Dtx + D
  Dx*, Dy* >> Dx Dx** >> Dx*
  The larger the surface to be averaged, the higher its value,
  It also exists in laminar flow!

## Slide 35
Order of magnitudes of diff. coefficient
10-8 10-6 10-4 10-2 1 102 104 106 108 cm2/s
Pore water
Molecular diff.
Vertical turbulent diff.
Deep layer surface layer
Cross-sectional dispersion (2D)
Long.dispersion (2D)
Longitudinal dispersion (1D)
Horizontal turbulent diff.
Tavak

## Slide 36
APPLICATION OF TRANSPORT EQUATION
Hydrodynamic equations  velocity distribution
3D transport eq.
Simplifications: 3D  2D, 3D  1D
Estimation of diffusion coefficient (measurements, empirical models)
Analytical solutions, or numerical methods
Non-conservative polluter: reaction kinetics terms( R(C) )

## Slide 37
Practical case: point source pollution in Danube river;
2D hydrodynamic and transport model

## Slide 38
Step 1:
Set up of the morphological model.
The figure shows the distribution of water depths.
The morphological model was based on
field measurements

## Slide 39
Step 2.
Velocity distribution [m/s] by 2D hydrodynamic model
(numerical solution);
Boundary conditions:
Upstream: flow rate of Danube river,
Downstream: Water level

## Slide 40
Step3.
2D transport model
Numerical solution for conservative substance.
Boundary condition: load [g/s] at the inflow point

## Slide 41
Determination of dispersion coefficient: tracer measurements

## Slide 42
Estimation of dispersion factors
Transverse dispersion factor(Fischer):
Dy* = dyu*R
R…Hydraulic radius
  dy – dimensionless constant,
    straight, regular channel: dy 0.15,
    Slightly winding bed: dy 0.2 – 0.6
  u* - bottom shear velocity, u* = (gRI)0.5
I…bottom slope
Longitudinal dispersion coeff. : dx 6