## Slide 1
DYNAMICS
Science of motion
STATICS
Science of rest (equilibrium)
The science of motion and rest
MECHANICS
KINEMATICS
The study of the description of the motion without considering the forces
The study of the of the motion by considering the forces
KINETICS

## Slide 2
The FORCE
It is and imaginary quantity which we use to express the mechanical action of a body to another one. It is a vector because it has a direction (line of action), a sense of action (its arrow) and a magnitude (unit N, kN). The length of the force vector is proportional to the magnitude of the force. For example 1cm (=) 1kN. This is called the force scale.
F
F’
Forces between two bodies always happen in pair and are opposite. Newton’s 3rd law.

## Slide 3
PROPERTIES OF FORCES SYSTEMS:
One can classifiy the force systems according to different points of view:
The dimension of the space: Forces in space (3D), forces in the plane (2D).
The relation between the lines of action:
  General
  Concurrent
  Parallel
The nature of the forces:
  Concentrated: unit: kN
  Distributed: unit: kN/m
In reality, there are only distributed systems of forces.
The concentrated force is an idealization.

## Slide 4
THE DATA OF A FORCE
Out of the vector of a force, an other information is necessary to fully charaterize a force and it is the so called point of application. The point of application can be any point of the line of action of the force because the force can be moved along its line of action.
y
So this point can be the intersection of the force with the x axis (xF).
So for a force in the plane there are to different but equivalent set od data.
analytical data: Fx, Fy, xF and
engineering data: F, α, xF .
In computations we always use the analytical data.
F
x
xF
α
Fy
Fx

## Slide 5
STATICS, the science of force sytems
There are two approches to study a discipline:
From the more complicated towards the simpler.
From the simpler towards the more complicated.
We chose the 2nd approach. The simplest forces system
in the plane is the system of concurrent forces. We start here.
The fondamental problems of statics: Equivalence and equilibrium.
The equivalence statement: ({Fi}) ({Qj})
The equivalence equations: = , =
Two concurrent force systems are equivalent if their force projection is the same in the x and y and z direction.
R

## Slide 6
The resultant:
It is a single force which is equivalent to a given force system.
The equivalence statement for the resultant: : R ({Fi})
The equivalence equations for the resultant: = , =
In 3D there is also = R is passing in the intersection point.

## Slide 7
EQUILIBRIUM
If the resultant vector of a concurrent for system is 0, then we say that the system is in equilibrium. We express it by the equilibrium statement:
({Fi}) 0 and the respective equilibrium equations:
= 0, = 0, = 0
F1
F3
F2
F3
VIEW
Vector diagram
Scale: 1cm (=) 1kN
F2
F1

## Slide 9
RF1 = 42.22*0.866-4.49*0.5 =34.22 N

## Slide 12
P6. The resultant of the forces (F1, F2, F3, F4 ) is a zero force (i.e. the forces are in equilibrium).
F1and F2 are given, and the directions of the forces F3and F4 are known.
Find the magnitude of F3and F4 .
2
F4 = 8/0.766 + 0.5/0.766*F3 →
7 – 0.866*F3 – 0.6428*(10.44+0.6527*F3) = 0 →
7-6.711-(0.866+0.6428*0.6527)*F3 = 0 → 0.289-1.2856*F3 = 0 →
F3 = 0.2247 kN, F4 = 10.44+0.6527*0.2247 = 10.59 kN
F3sin30ᵒ
-F3cos30ᵒ

## Slide 13
R13 is the resultant of R1 and R3
=
The system is in equilibrium
Length of F2, F4.

## Slide 14
Geometric Conditions of the Equilibrium of Three Forces
Fundamental theorem
1) The three forces should be concurrent.
2) They should be in the same plane.
3) The vector triangle formed from them should be closed and continuous.
View
F1
F2
F3
F1
F2
F3
Vector diagram
1 cm (=) 1 kN

## Slide 15
P8. The resultant of the forces (F1, F2, F3 ) is a zero force (i.e. the forces are in equilibrium).
F1 is given, the direction of the force F2 and the magnitude of the force F3 is known.
Find the magnitude of F2 and the direction of F3 .
F1+F2+F3 = 0 The resultant vector is 0. This means that the vector diagram is closed and continuous in arrow.
The grapho-analytical method: We observe the properties of the vector diagram and we use computation to obtain the result.
t
F2
F1 = 5
F3,II
F3,I
90-α
α
α
h
s
F1,2
ΣFit = 5*cos60ᵒ – 4*cosα = 0
α3t = 51.32ᵒ
F2,II
F2,I
h =
5*sin30ᵒ
= 2.500
s =
h*tan(α)
s =
2,500*tan(51.32ᵒ)=
F1,2 =
5*cos30ᵒ =
4.330
F2,I =
F1,2 – s =
1.207kN
F2.II =
F1,2 + s =
7.453 kN
F3
F3
F2
F3 = 4kN
3.123
t
30⁰
30⁰

## Slide 16
F2.II =
F1,2 + s =
7.453 kN
t
F2
F1 = 5
F3,II
F3,I
90-α
αt3
α
h
s
F1,2
ΣFit = 5*cos60ᵒ – 4*cosα = 0
α3t = 51.32ᵒ
F2,II
F2,I
h =
5*sin30ᵒ
= 2.500
s =
h*tan(α)
s =
2,500*tan(51.32ᵒ)=
F1,2 =
5*cos30ᵒ =
4.330
F2,I =
F1,2 – s =
1.207kN
If a force system is in equilibrium then its projection to any axis is 0.
Data
NoNo | F | αx
1 | 5 | 60
2 | ? | 30
3 | 4 | ?
How do we construct the solution?
1) We define an axis t which is perpendicular to the direction of F2, so has 30⁰ to the y axis.
30⁰
30⁰
30⁰
Solution géométrique
F1
F3
F2