## Slide 1: Surveying II
Geodetic deformation analysis, subsidence monitoring.
Dr. Lóránt Földváry
25 May, 2023

## Slide 3: Geodetic deformation analysis, horizontal and vertical monitoring
Regardless the task is monitoring of displacement or deformation, the structure is modelled by a set of its characteristic points, and the monitoring is carried out by determining their 3D coordinates at different times.
Surveying techniques are very suitable for this purpose.

## Slide 4: Properties of geodetic deformation analysis
structures are identified by some of their points, which should be selected in places relevant for the analysis, furthermore, their stability by time should be ensured
the method of the measurement should be chosen to allow the detection of the displacement with the demanded accuracy
the motion of the test points are determined to fix reference points (spatial reference)
the motion of the test points are determined relatively to a baseline measurement performed at the start of the analysis (temporal reference)

## Slide 5: The direction of the motion is known
Offset survey
A baseline is set perpendicular to the direction of the motion, and the test points are set near to the line joining the reference points.

## Slide 6: The direction of the motion is known
a – measuring small angles, b – using adjustable point marker
Offset survey
instrument
instrument
pole / prism
pole / prism
test point
test point
scale

## Slide 7: The direction of the motion is known
a – measuring small angles, b – using adjustable point marker
Offset survey

## Slide 8: The direction of the motion is known
An elongated traverse line is established perpendicular to the direction of the displacement, with the start and end points located on a motion-free area.
Measuring the length of the traverse legs only at the first epoch, while deflection angles measured each time.
A coordinate system is established by setting the y-axis through the start and end points.
The displacement of the points is detected via the change of the x-coordinates.
y
x
S
E

## Slide 9
In such cases either a baseline or a network is established in a local coordinate system. (Measurements on the baseline processed by intersections, measurements in network are processed by network adjustment).
All relevant coordinate components (2D, 3D) are determined at different epochs.
Based on the components, the vector of the displacement (direction, magnitude) can be determined.
The direction of the motion is unknown

## Slide 10
The direction of the motion is unknown
In such cases either a baseline or a network is established in a local coordinate system. (Measurements on the baseline processed by intersections, measurements in network are processed by network adjustment).
All relevant coordinate components (2D, 3D) are determined at different epochs.
Based on the components, the vector of the displacement (direction, magnitude) can be determined.
Scale
- displacements
- network

## Slide 11: The direction of the motion is unknown
Inter- and resections
intersection
arc section
resection
side section

## Slide 12
The horizontal displacement of inaccessible, high points of tall, slender structures (towers, smokestack) can be determined by intersection (using WCB).
The baseline is set at a distance of 2-3 times the height of the test points, and the structure is visible at nearly perpendicular direction from the basepoints.
Hz angle measurements are made from two basepoints.
Teodolit „A”
Teodolit „B”
The direction of the motion is unknown

## Slide 13: The direction of the motion is unknown

## Slide 14: Observation of displacement of inaccessible points with electrical method
In the coil of differential transformers, the inductance changes inversely to motion of the magnetic core.
The coil is operated by alternating current (AC). The change of inductance can be measured with a Wheatstone bridge.
magnetic core
linear measurement range
voltage
displacement, ΔL

## Slide 15: Monitoring subsidence
Subsidence means change in height, therefore monitoring can be done by precise measurement of height differences.
Classic method for subsidence monitoring is levelling.
Trigonometric heighting can applied, if:
  for shorter than 100 m distances;
  for test points allowing precise sighting, and with zero target height;
  using trigonometric levelling, in which there is case no need of measuring the instrument height.
Inside buildings, hidrostatic leveling can be performed.

## Slide 16: Planning the process of subsidence monitoring
test points should be located at the maximum expected vertical displacements;
test points should be set by permanent marking, and they should be protected against damage;
avoid use of temporary marking (change plate), so the distance between the instrument and the staff (test points) should be not greater than 25 m;
Networks inside a building should connected to external reference points at least at two legs;
the reference points should be established at fix places: at least two groups should be established with at least three points per group;
the stability (no displacement) of the reference points should be checked at least once a year.

## Slide 17
Accuracy planning of subsidence monitoring
Define the minimal subsidence demanded to be detected (D),
Determine the mean error of a single height difference (mDm).
A levelling line should be run between two points with known height. The least accurate point of line levelling is at the middle of the line.
Accordingly: the mean error of the height of the midpoint (mm) should be calculated.
A line with n stands:

## Slide 18
Subsidence is the difference of two height values, so mean error of the subsidence (mD) is times of the mean error of a height (mm).
Accuracy planning of subsidence monitoring
In case of a line with n stations:
The maximum of the mean error () cannot exceed the minimal subsidence to be detected (D):

## Slide 19
How to determine the maximal number of stations?
thus
(n should be rounded downward to the closest integer.)
Accuracy planning of subsidence monitoring

## Slide 20: Hydrostatic levelling
Based on the principle of communicating vessels: liquid balances out to the same level in all of the containers regardless of the shape and volume of the containers.
A pipe is used with its two ends fixed below the test points. Due to subsidence, a change of the vertical distance between the test point and the water surface can be observed.

## Slide 21
Hydrostatic levelling
A pipe is used with its two ends fixed below the test points. Due to subsidence, a change of the vertical distance between the test point and the water surface can be observed.

## Slide 22: Hydrostatic levelling
A pipe is used with its two ends fixed below the test points. Due to subsidence, a change of the vertical distance between the test point and the water surface can be observed.
Hydrostatic levelling does not detect subsidence of the whole object, so for a full subsidence measurement it is supported by optical levelling to fix reference points.

## Slide 23: Hydrostatic levelling
With precise hydrostatic measuring systems accuracy of nanometres can be achieved.
To achieve this, systematic errors (varying temperature of the filling liquid, air pressure differences at free pipe ends, tidal effects) are minimized; also, the water level is measured using capacitive / ultrasonic / vibrating string methods.
Typical applications of such systems are: precise subsidence monitoring, electron accelerators

## Slide 24: Hydrostatic levelling
A common disadvantage of hydrostatic levels is that the height difference between the test points cannot exceed 10-20 cm.
If the subsidence exceeds this, by using an appendage made of invar (FeNi36, a nickel–iron alloy, special about its low thermal expansion), the test points can be brought close to the reference level surface.

## Slide 25: Results of deformation analysis
Numerical tables
no. of measurement | 0 | 1 | 2 | 3
epoch [year] | 1991 | 1993 | 1996 | 2001
height [m] | 104.4948 | .4920 | .4890 | .4843
Dm = mi – mi-1 | - | -2.8 | -3.0 | -4.7
Dm = mi – m0 | - | -2.8 | -5.8 | -10.5
no. of measurement | 0 | 1 | 2 | 3
epoch [year] | 1991 | 1993 | 1996 | 2001
height [m] | 104.3665 | .3633 | .3599 | .3555
Dm = mi – mi-1 | - | -3.2 | -3.4 | -4.4
Dm = mi – m0 | - | -3.2 | -6.6 | -11.0
Subsidence of point P
Subsidence of point Q

## Slide 26: Results of deformation analysis
mean error of subsidence ±1,0 mm
epoch [year]
subsidence [mm]
Graphical visualization
Scale
- displacements
- network

## Slide 27: Results of deformation analysis
Subsidence of a building can be visualized by displaying the subsidence of the test points in axonometric view.
5 mm
10 mm
0
a
mean error of subsidence: average ±0,84 mm
maximal ±1,18 mm
Q
Q
P
P
b
Graphical visualization

## Slide 28: Results of deformation analysis
Q
P
Q
P
0
0
1
-1
-2
-1
-1
-2
-3
-4
-5
-1
-2
-3
-1
0
1
-5
-10
a
b
Subsidence can also be visualized by showing linearly interpolated contour map (isolines) of the subsidence based on the test points.
Graphical visualization

## Slide 29
Automatized, quasi continuous measurements (total stations with servomotor, ATR)
Alarm can be raised real time in case of a critical situation
Monitoring systems

## Slide 30: Monitoring systems
Localization tower:
- structure: appr. 25x40x50 m reinforced concrete
- wall thickness: 1.5 m
- aim: lock radioactive contamination inside in case of malfunction
- requirement: it should bear overpressure

## Slide 31: Monitoring systems
Automatization: total stations equipped with servomotor, ATR

## Slide 32: Monitoring systems
West facade
North facade

## Slide 33: Monitoring systems
Siki – Takács – Égető

## Slide 34: Further sensors for deformation analysis
Strain gauge
Method: the eigenfrequency of a strained string is observed
Aim: observe tensile strain of steel beams between slurry walls
Automatized data acquisition (20 min.)
Frequency -> displacement

## Slide 35: Further sensors for deformation analysis
Tiltmeter
MEMS
a mechanical component for observing tilt / acceleration is integrated into a printed circuit board (PCB)
wide measurement range, ±45°
accuracy: 0.0001°(0.00175 mm/m)
measurement mode: dynamic
Electrolytic
electrodes dipped in electrolytic liquid detect the change of resistance due to change in tilting
narrow measurement range, ±0.6°
accuracy: 0.0003°(0.005 mm/m)
measurement mode: static

## Slide 36: Further sensors for deformation analysis
GNSS-receivers

## Slide 37: Further sensors for deformation analysis
GNSS-receivers
battery
Clients
Redundant
servers

## Slide 38: Further sensors for deformation analysis
GNSS-receivers

## Slide 39: Thank you for the attention!